## Slide 1: Driving a robot with one forearm
AWARE-AI Hackathon 2026
AJ · Jose · Kiran · Xinyi
Notes: (AJ) Hi, I'm AJ, and with me are Jose, Kiran and Xinyi. In the next five minutes we'll show you how we drive the Jackal with one forearm and a Myo armband, what the muscle and motion signals taught us, and the results from the sim. Here's the plan.

## Slide 2: Five parts, about a minute each
Agenda
1 · How you drive
2 · What the signals told us
3 · Calibration, assistance, safety
4 · What broke
5 · Results
Notes: Five parts. How a driver controls the robot. What the signals told us, which is why our design looks the way it does. How a new driver calibrates, and what keeps the robot safe. What broke while we tested. And the results. First, what we built.

## Slide 3: One forearm drives every course, with no collisions
What we did
20.7 s
L1 Gates
median of 4 runs, 0 collisions
26.6 s
L2 Slalom
median of 6 runs, 0 collisions
16.3 s
L3 Corridor + Dock
median of 4 runs, 0 collisions
51 of 51 runs finished. New driver: 2 minutes to calibrate.
Score = time + 5 s per collision + 10 s per missed gate (the sim's rule). Lower is better.
Notes: Here's what we built. One forearm and the Myo armband drive all three courses. Over 51 official runs we finished every single one, with no missed gates and no collisions on the clean courses. Why should you care? A new driver records their own calibration in about two minutes, and it kept working under the judges' slow, lossy link. So how do you drive it?

## Slide 4: Arm height sets speed, roll steers
1 · How you drive
STOP · arm up
GO · level
REVERSE · tip down
elbow
STEER · roll the forearm
like turning a doorknob, left or right; a bigger roll turns harder
BRAKE · firm fist
held for 0.4 s; your hand stays relaxed the rest of the time
Raise the arm once to start. Lower = faster, up to full speed at level.
Notes: The arm is the joystick. Raise your forearm and the robot stops. Lower it to level and it drives, and the lower you go toward level, the faster. Tip it down past level and it backs up. Roll your forearm like a doorknob to steer. And if something goes wrong, make a firm fist and hold it for under half a second: that's the brake. Your hand stays relaxed the whole time, so it isn't tiring. Why not just use muscle gestures? We tried.

## Slide 5: Muscle gestures broke once the forearm rolled
2 · What the signals told us
Still poses (all 5 gestures)
99% read correctly
Fist held with the forearm rolled
38% read correctly
Rolled fists misread as: right 53, reverse 51, left 8 of 181 windows
Classifier: linear discriminant analysis on 8 EMG channels, tested on takes it never trained on.
Notes: We started with five muscle gestures and a classifier. On still poses it was right 99% of the time, on takes it had never seen. But hold a fist with your forearm rolled, which is exactly what you do while steering, and it read "forward" only 38% of the time. The rest came out as right, reverse or left. Rolling your arm moves the muscles under the electrodes. So we kept the muscle signal for the brake only, and steer with the band's tilt sensor, which rolling can't fool.

## Slide 6: A neural network didn't beat the simple model on our data
2 · What the signals told us
Trained on your own calibration
TCN 68%
LDA 85%
Tested on a new driver
TCN 33%
LDA 32%
chance 17%
TCN: neural network on the raw signal. LDA: linear model on 16 features. Share of 200 ms windows read as the right pose; bar: median of 4 drivers, line: lowest to highest. New driver: each scaled by their own calibration.
Notes: (AJ) We also asked whether deep learning would read the muscles better. We trained a temporal convolutional network on the raw signal, with gain and noise augmentation, and tested it on takes and drivers it never saw. On each person's own two-and-a-half-minute calibration, the simple linear model still won: 85% of poses against 68%. On a driver it had never seen, both were near 32%, against seventeen percent for guessing. With this little data per person, the simple model is the right choice, so the controller keeps it for the brake.

## Slide 7: Ready in two minutes, and it stops when unsure
3 · Calibration, assistance, safety
1
Record
6 poses × 2, 3, 5 s
2
Hold straight
2 s at every start
3
Raise to start
arms the robot
4
Drive
speed, steer, brake
The robot stops when:
the signal drops
the arm leaves its range
the band has moved (won't start)
a fist is held 0.4 s
Notes: Every driver records their own calibration: six poses, each held for two, three and five seconds, about 2 minutes in all, with prompts. At the start of each drive they hold their arm straight for two seconds, so straight is straight for them. Then they raise the arm to arm it. Underneath, the robot stops whenever it's unsure: if the signal drops, if the arm leaves its calibrated range, or if the band has moved, in which case it refuses to start and asks for a new calibration.

## Slide 8: Four drivers calibrated with one command
3 · Calibration, assistance, safety
python examples/lever.py <your name>
AJ
9.7×
Jose
4.6×
Xinyi
4.0×
Kiran
1.9×
Kiran, 1st try
0.6×
Fist ÷ relaxed muscle level (mean RMS over 8 channels). Below 1×, the fist didn't register.
Notes: (Kiran) To get past one driver, we made setup a single command. It connects the Myo, records your calibration, opens the sim and drives. Four of us recorded, and the data is public. The bars show how much stronger each person's fist is than their relaxed hand, which is what the brake detects. My first recording came out below one: the fist didn't register, so I recorded again. Now the tool shows that check after every calibration.

## Slide 9: The gate assist nudges you through, and never steers for you
3 · Calibration, assistance, safety
2 of 6
approaches through gate 1 with the assist
0 of 6
without it
0
collisions, either way
only when you're aimed within 20° of a gate
adds at most 0.3 rad/s of turn
never picks a gate for you
off with --no-gate
Scripted off-line approaches to L1's first gate in the sim, the same assist code as the controller.
Notes: (Xinyi) I added a gate assist. The lidar finds the two posts of the next gate. If you are already aimed within twenty degrees of it, it adds a small correction toward the centre, never more than 0.3 radians per second, so you stay in control. In 6 test approaches from off the line, it got through the first gate 2 times against 0 without it, with no collisions either way. When the approach wasn't aimed at the gate, it did nothing.

## Slide 10: Four things broke; each fix is now a rule
4 · What broke
Problem
Before
Fix
After
Brake fired by itself
38% of drive time
fist pattern held 0.4 s
0%
Right turns too weak
full turn out of reach
each side tuned from your own drives
even turns
Band moved after charging
reversed 58% of a drive
pose checked at every start
refuses to start
Myo vanished after unplugging
no Myo found
wear it, move, keep scanning
connects
Notes: (Jose) Four things broke. First, the brake fired on its own 38% of the time, because just holding your arm out uses the same forearm muscles. Now it needs a fist pattern held for 0.4 seconds, and it dropped to zero. Second, right turns were weak: with the arm out you only roll about thirty degrees right, so we tune each side from the driver's own logs. Third, after a battery recharge the band went back on differently and the robot reversed 58% of the time. Now it checks the pose at every start and refuses if the band moved. And today the Myo vanished: once unplugged it fell asleep and no laptop could find it. Wearing it and moving while the tool keeps scanning brought it back, and that's in our troubleshooting guide.

## Slide 11: All 51 official runs finished, with no missed gates
5 · Results
L1 Gates
20.7 s
L2 Slalom
26.6 s
L3 Corridor + Dock
16.3 s
L1, 300 ms lag + 10% drop
21.7 s
Bar: median score. Line: best to worst run. Clean courses: 4, 6 and 4 runs; degraded: 8 runs with lag compensation on.
Notes: Here are the official scores, the medians over repeated runs so it isn't one lucky lap: 20.7 seconds on L1, 26.6 on the slalom, 16.3 on the corridor and dock, with no collisions. The last bar is L1 under the judges' degraded link, 300 milliseconds of lag and ten percent packet loss: about 21.7 seconds, barely slower than clean. That's the robustness we were after. Speaking of lag, we tested one more idea.

## Slide 12: Lag compensation did no harm; benefit unproven
5 · Results
Lag compensation on
median 21.7 s
Off
median 22.5 s
20 s
22 s
24 s
26 s
28 s
One dot per run, L1 at 300 ms lag and 10% drop, 2 runs per hidden session. Session medians compared with an exact two-sided permutation test: p = 0.57 for score, 0.26 for workload.
Notes: With 300 milliseconds of lag, drivers overcorrect, so we added lag compensation: it measures the delay, softens steering, and checks obstacles from where the robot will be when each command lands. To test it fairly we ran it blind: 8 sessions, the controller secretly switching it on or off, so the driver couldn't know. With it on, the medians were a little better and there were no collisions, against 2 without. But with this few runs, the difference isn't significant. We kept it on because it did no harm.

## Slide 13: What we'd test next
5 · Results
1
More people
Pretrain on a 36-person Myo dataset, fine-tune on each driver's 2-minute calibration.
2
Lag gain unproven
More blind sessions before we claim lag compensation helps.
3
Top speed 1 m/s
The sim allows 2 m/s: the assist must slow from further out first.
Notes: (AJ) What we'd do next. Four drivers isn't enough for a neural network, so we'd pretrain on a public Myo dataset of thirty-six people, which has the relaxed hand and the fist the brake needs, then fine-tune on each calibration. The lag result needs more sessions before we'd claim it helps. And we capped speed at one metre per second while tuning, half what the sim allows, so going faster means the obstacle assist has to look further ahead first.

## Slide 14: Thank you
AJ · Jose · Kiran · Xinyi
Code and dataset: github.com/ajbarea/Hackathon
Notes: That's our controller: one forearm, no squeezing, every course finished. The code and the dataset are public on GitHub. Thank you, and we're happy to take questions.

## Slide 15: Backup slides
Notes: Backup slides for questions.

## Slide 16: Blind lag-compensation test, session by session
Backup
Measure | On | Off | p
Score (s) | 21.66 | 22.51 | 0.57
Steering jerkiness (rad/s²) | 0.66 | 0.74 | 0.63
Workload (NASA-RTLX, 0 to 100) | 43.4 | 50.4 | 0.26
Collisions (total) | 0 | 2 | –
4 sessions on, 4 off, 2 runs each; the driver never knew which.
Notes: Backup. The blind test in full: medians of each session's two runs, compared with an exact two-sided permutation test.

## Slide 17: How the signals are used
Backup
Signal | What we compute | Drives
Tilt (accelerometer, 50 Hz) | forearm height and roll from gravity, never yaw (no drift) | speed, steering, reverse
Muscle (8 EMG channels, 200 Hz) | RMS and waveform length per channel, 0.2 s windows | brake only
Brake classifier | your fist vs your other poses (linear discriminant analysis) | fist held 0.4 s
Lidar (from the sim) | free space ahead and beside the robot | slow down, nudge off walls
Notes: Backup. What each signal does: the tilt sensor gives speed, steering and reverse; the muscle signal only gives the brake.