## Slide 1: Driving a robot with one forearm
AWARE-AI Hackathon 2026
AJ · Jose · Kiran · Xinyi

## Slide 2: Five parts, about a minute each
Agenda
1 · How you drive
2 · What the signals told us
3 · Calibration, assistance, safety
4 · What broke
5 · Results

## Slide 3: One forearm drives every course, with no collisions
What we did
20.7 s
L1 Gates
median of 4 runs, 0 collisions
26.6 s
L2 Slalom
median of 6 runs, 0 collisions
16.3 s
L3 Corridor + Dock
median of 4 runs, 0 collisions
51 of 51 runs finished. New driver: 2 minutes to calibrate.
Score = time + 5 s per collision + 10 s per missed gate (the sim's rule). Lower is better.

## Slide 4: Arm height sets speed, roll steers
1 · How you drive
STOP · arm up
GO · level
REVERSE · tip down
elbow
STEER · roll the forearm
like turning a doorknob, left or right; a bigger roll turns harder
BRAKE · firm fist
held for 0.4 s; your hand stays relaxed the rest of the time
Raise the arm once to start. Lower = faster, up to full speed at level.

## Slide 5: Muscle gestures broke once the forearm rolled
2 · What the signals told us
Still poses (all 5 gestures)
99% read correctly
Fist held with the forearm rolled
38% read correctly
Rolled fists misread as: right 53, reverse 51, left 8 of 181 windows
Classifier: linear discriminant analysis on 8 EMG channels, tested on takes it never trained on.

## Slide 6: A neural network didn't beat the simple model on our data
2 · What the signals told us
Trained on your own calibration
TCN 68%
LDA 85%
Tested on a new driver
TCN 33%
LDA 32%
chance 17%
TCN: neural network on the raw signal. LDA: linear model on 16 features. Share of 200 ms windows read as the right pose; bar: median of 4 drivers, line: lowest to highest. New driver: each scaled by their own calibration.

## Slide 7: Ready in two minutes, and it stops when unsure
3 · Calibration, assistance, safety
1
Record
6 poses × 2, 3, 5 s
2
Hold straight
2 s at every start
3
Raise to start
arms the robot
4
Drive
speed, steer, brake
The robot stops when:
the signal drops
the arm leaves its range
the band has moved (won't start)
a fist is held 0.4 s

## Slide 8: Four drivers calibrated with one command
3 · Calibration, assistance, safety
python examples/lever.py <your name>
AJ
9.7×
Jose
4.6×
Xinyi
4.0×
Kiran
1.9×
Kiran, 1st try
0.6×
Fist ÷ relaxed muscle level (mean RMS over 8 channels). Below 1×, the fist didn't register.

## Slide 9: The gate assist nudges you through, and never steers for you
3 · Calibration, assistance, safety
2 of 6
approaches through gate 1 with the assist
0 of 6
without it
0
collisions, either way
only when you're aimed within 20° of a gate
adds at most 0.3 rad/s of turn
never picks a gate for you
off with --no-gate
Scripted off-line approaches to L1's first gate in the sim, the same assist code as the controller.

## Slide 10: Four things broke; each fix is now a rule
4 · What broke
Problem
Before
Fix
After
Brake fired by itself
38% of drive time
fist pattern held 0.4 s
0%
Right turns too weak
full turn out of reach
each side tuned from your own drives
even turns
Band moved after charging
reversed 58% of a drive
pose checked at every start
refuses to start
Myo vanished after unplugging
no Myo found
wear it, move, keep scanning
connects

## Slide 11: All 51 official runs finished, with no missed gates
5 · Results
L1 Gates
20.7 s
L2 Slalom
26.6 s
L3 Corridor + Dock
16.3 s
L1, 300 ms lag + 10% drop
21.7 s
Bar: median score. Line: best to worst run. Clean courses: 4, 6 and 4 runs; degraded: 8 runs with lag compensation on.

## Slide 12: Lag compensation did no harm; benefit unproven
5 · Results
Lag compensation on
median 21.7 s
Off
median 22.5 s
20 s
22 s
24 s
26 s
28 s
One dot per run, L1 at 300 ms lag and 10% drop, 2 runs per hidden session. Session medians compared with an exact two-sided permutation test: p = 0.57 for score, 0.26 for workload.

## Slide 13: What we'd test next
5 · Results
1
More people
Pretrain on a 36-person Myo dataset, fine-tune on each driver's 2-minute calibration.
2
Lag gain unproven
More blind sessions before we claim lag compensation helps.
3
Top speed 1 m/s
The sim allows 2 m/s: the assist must slow from further out first.

## Slide 14: Thank you
AJ · Jose · Kiran · Xinyi
Code and dataset: github.com/ajbarea/myo-lever

## Slide 15: Backup slides

## Slide 16: Blind lag-compensation test, session by session
Backup
Measure | On | Off | p
Score (s) | 21.66 | 22.51 | 0.57
Steering jerkiness (rad/s²) | 0.66 | 0.74 | 0.63
Workload (NASA-RTLX, 0 to 100) | 43.4 | 50.4 | 0.26
Collisions (total) | 0 | 2 | –
4 sessions on, 4 off, 2 runs each; the driver never knew which.

## Slide 17: How the signals are used
Backup
Signal | What we compute | Drives
Tilt (accelerometer, 50 Hz) | forearm height and roll from gravity, never yaw (no drift) | speed, steering, reverse
Muscle (8 EMG channels, 200 Hz) | RMS and waveform length per channel, 0.2 s windows | brake only
Brake classifier | your fist vs your other poses (linear discriminant analysis) | fist held 0.4 s
Lidar (from the sim) | free space ahead and beside the robot | slow down, nudge off walls